DIGITAL LOGIC DESIGN

ASSIGNMENT - 1

NUMBER SYSTEM

PART – 1

NUMBER SYSTEM CONVERSION

Ex-1 Convert Following Decimal Number into Binary, Octal & Hexadecimal Number.

- 37					5.	132

- 197.625				6.	220.55

- 33.5675				7.	89.345

- 80.100

Ex-2 Convert Following Binary Number into Decimal, Octal & Hexadecimal Number

- 10110					5.	10110101

- 101010.10				6.	11011.1101

- 1101100.011				7.	10001.10001

- 1111.1111

EX-3	Convert Following Hexadecimal Number into Binary, Octal & Decimal Numbers

- (CD) h					5.	(FF) h

- (78) h					6.	(4C1D.A) h

- (89FF) h				7.	(AA.BB) h

- (1A2B.3C) h

EX-4	Convert Following Octal Number into Binary, Decimal & Hexadecimal Numbers

- (77)o					4.	(156)o

- (55.40)o				5.	(147.72)o

- (50.40)o				6.	(564.23)o

EX-5   Convert following numbers.

1.	(1022)3  =   (            ) 4    =   (            ) 9     >>> Base 3 to base-4 and base-9

2.	(AB.D)H  =   (            ) 3   =   (            ) 5     >>> Base 16 to base-6 and base-5

3.	(12.34) 8  =   (            ) 4   =   (            ) 7     >>> Base 8 to base-4 and base-7

4.	(125.34) 6  =   (            ) 8   =   (            ) 7     >>> Base 6 to base-8 and base-7

PART-2

COMPLEMENT

EX-6 	Find 9’s & 10’s Complement for the following decimal number

- 89					5.	183.34

- 146					6.	878.100

- 687.93					7.	903.90

- 9999

EX-7	Find 12-bit 1’s & 2’s Complement for the following binary number

- 1011					4.	10110

- 1001010				5.	10100.111

- 1001001.1001				6.	11111.11111

Ex-8	Find 12-bit 1’s complement & 2’s complement form of following decimal numbers.

- -37					5.	-173

- -97					6.	-244

- -65.5					7.	-197.5

- -205.6					8.	-29.375

Ex-9	Represent following decimal Numbers in 8-bit

- Sign Magnitude Form

- Sign 1’s Complement Form

- Sign 2’s Complement Form

- +14					4.	+27

- +45					5.	-17

- -47					6.	-100

- -127

PART-2

ADDITION & SUBTRACTION

Ex-11	Subtract following decimal Numbers using both 9’s & 10’s Complement

- 274 – 86				5.	93 – 615

- 1000 – 738				6.	546.4 – 279.7

- 376.8 – 765.6				7.	788.898 – 432.139

- 9999 – 10000

Ex-12	Add Following Binary Numbers

- 11011 + 1101				4.	1101 + 1011 + 0110

- 101110.110 + 111.10101		5.	11001.10001 + 11.010101

- 11111.111  + 10101.1			6.	1010.10 + 1101.10 + 1001.11

Ex-13	Subtract Following Binary Numbers

- 1011 – 101				3.	10110 – 1011

- 1101.10 – 111.11			4.	10111.01 – 111.11

Ex-14	Subtract Following Decimal Numbers using the 12-bit 1’s complement & 2’s Complement arithmetic.

- 46 – 19				4.	27 – 75

- 46 – 84				5.	63.75 – 17.5

- 125.6 – 46.7				6.	36.78 – 89.5